## Slide 2
SCG LMH 2021 – Performance to Operations
2020 CW 49

## Slide 3: Issue list

## Slide 4: 1 – Fuel saving strategy
Before each track event, we can prepare tables like this from simulation
Note: it was suggested to have a specific function on the dashboard to inform the driver about the correct lift and coast duration: in meters or time?
Straight number |  | 1 | 2 | 3
Lift and coast | m (s) |  |  | 
Fuel saving | kg (l) |  |  | 
 | % |  |  | 
 | laps / lap |  |  | 
Lap time cost | s |  |  | 
Questions:
Can this information be integrated in HH Timing?
Should we do something different?
Is it manageable from the driver to request coasting on more than 1 point on the track?
Feedback:
…

## Slide 5: 2 – Tyre stints at Le Mans
Information from Michelin:
There will be 3 dry specs, each race 2 of these specs will be brought at Michelin discretion (a softer and a harder one)
There will be 2 wet specs: it’s the same tire with little machining, that can be requested with deeper manual grooving by Michelin technician
At Le Mans there will be all 3 dry specs available
The target from Michelin will be to allow from 2 to 3 stints of 12 laps in Le Mans (depending on pressure and camber levels, tables still not ready)
Pressure indication will not be a “cold” or heat blanks pressure, but a lap average value from TPMS data
Questions:
…
Feedback:
…

## Slide 6: 3 – Brake wear prediction
We don’t have information about material consumption vs dissipated energy from AP Racing (we can try to ask again)
Indication is to avoid going above 650°C to avoid oxidation, this way AP indicates that is possible to cover the full 24h race of Le Mans. No indications for other tracks.
We have models to predict brake temperature over the lap, which are based on CFD data for the brake duct inlet velocities and lap simulations
We can validate it in 5 steps:
Validate in the WT full scale test the CFD brake duct flow VS ride height and speed, at front and rear
Validate with track data from the shakedown or 1st performance test the brake temperature prediction, and experimentally evaluate brake material wear vs dissipated energy per lap
Validate the brake energy per lap from simulation
Validate at the track brake temperature vs inlet blanking
Predict by simulation the brake temperature and brake wear for the most demanding races
Questions:
Can this process work?
Is it done differently in the current state-of-art?
Feedback:
…

## Slide 7: 4 – Strategy software
It has been indicated that HH Timing is probably the best option.
From initial interviews with potential race engineers it is confirmed that either they know the HH Timing or know its potential
Race strategy will be something to be managed between the Race Engineer(s) – Performance Engineer and the Strategy Engineer (?)
Worth having a dedicated discussion once the Race engineers will be onboard (official target is January 2021), once the roles are confirmed it is probably possible to kick off the discussions, even if not with a full-time availability.
Questions:
…
Feedback:
…

## Slide 8: 5 – Sheets
Something is being prepared, although the feedback from Race Engineers would be necessary to ensure all the involved people are happy with them.
It is possible to at least confirm a list of sheets to be prepared:
Car setup (version for engineers, with more data)
Car setup (version for the chief mechanic, with the mechanical information equivalent to the number the race engineer sees)
End of stint task list 1 for the chief mechanic (standard tasks)
End of stint task list 2 for the chief mechanic (setup changes or specific requests from the race engineer due to issues spotted by the support engineers)
Track event planning (with distinction between car 1 and car 2, aero car and ride car? Try to test more things with two cars)
Chief mechanic to race engineer feedback sheet (can it be part of the task lists?)
More??
Questions:
…
Feedback:
…

## Slide 9: 6 – Conversion tables for mechanics
Agreed in the operations meeting 2020CW49 that the design team will provide those
Questions:
…
Feedback:
…

## Slide 10: 7 – Shakedown planning
Detailed planning under preparation, currently the proposed topics are:
Day 1:
Ensure car is not touching the ground (especially end of straight speed, ride heights, which are predicted from aero maps)
Torque control calibration
Gear shift calibration
Engine vital parameters check (pressures, temperatures, lambda, knock..)
Day 2:
Minimal aero validation (coast downs at different ride heights, we can conveniently use the third spring to achieve the desired RH)
Constant radius cornering (since we have a skid-pad at Vairano worth using it). To collect understeer characteristic data and validate simulation, possibly with at least 3 speeds and 3 roll stiffness setups (3 runs, no more than 1h)
Enable a minimal traction control for car protection
Initial calibration of the control on the maximum driveshaft power
To be further discussed: any feedback is welcome
Feedback:
…

## Slide 11: 8 – 1st Performance test planning
The main target of performance test 1 will be to fix what cannot be changed after homologation
Brake cooling outer ring
Brake cooling inlet blanking options
RW position (if anything meaningful can be tested on track, to be understood within the regulation limits for drag and downforce)
More?
Obviously not all the time will be spent for this, and maybe we don’t need specific tests for some of these things.
Other priorities:
More aero track data collection (if necessary)
Setup refinement (heave and roll stiffnesses, damping only if necessary)
Traction control calibration
To be further discussed: any feedback is welcome
Feedback:
…